File	DIS_PKT.DOC						18 May 1991
From:	Joe R. Doupnik
	Utah State University
	Logan Utah 84322
	jrd@cc.usu.edu
	(801) 750-2982 voice
	(801) 750-2992 fax

What DIS_PKT.DOS does: It provides an Ethernet-like Packet Driver
interface to programs built to operate over Packet Drivers. It talks
to NDIS (3Com/Microsoft) instead of to a lan board directly. It shares
the board with NDIS users. We call this a "shim", sitting between the
normal applications program (NetWare shells, TCP/IP, etc) and the more
hardware specific portions (NDIS in this case).

    Packet Driver flavored applications		NDIS flavored applications
		||					||
	    -------------				||
	    |  DIS_PKT  |				||
	    -------------				||
		||					||
		------------------------------------------
		|           main module			  |
		|   NDIS    ........................      |
		|	    board specific driver(s)	  |
		-------------------------------------------
				  ||
			-------------------------
			|    Ethernet board(s)	|
			-------------------------
				  ||
		=========================================== Ethernet wire
		

First sample PROTOCOL.INI file:

[protocol manager]
    drivername = PROTMAN$

[pktdrv]			<-- name of this driver entry
  drivername = pktdrv$		<-- formal driver name
  bindings = wd8003xmac		<-- use your board's NDIS driver here
  intvec = 0x60			<-- Packet Driver Int, 60h..7fh
  chainvec = 0x66		<-- daisy chained Pkt Drvr Int, unused

[attiso]
  drivername = ATTISO$		<-- Another NDIS client
  bindings = wd8003xmac		<-- bound to the same harware driver
  nsess = 5
  ncmds = 14
  use_emm = n

Western Digital EtherCard PLUS Family Adapter	<-- Ethernet board
[wd8003xmac]					<-- its ndis driver
    drivername = MACWD$
    irq = 7
    ramaddress = 0xCA00
    iobase = 0x280
    receivebufsize = 1536	<-- make this a full Ethernet pkt




Sample section of CONFIG.SYS (StarGROUP material is not required):

device=c:\lanman\protman.sys /i:c:\lanman	<-- must be first
device=c:\lanman\macwd.dos			<-- WD8003E driver
device=c:\lanman\dis_pkt.dos			<-- Pkt Driver (this program)
device=c:\lanman.dos\drivers\attload.dos /Y	<-- StarGROUP NDIS 
device=c:\lanman.dos\drivers\attiso\attiso.dos	<-- StarGROUP NDIS
device=c:\qemm\loadhi.sys /r:1 e:\pctcp\ifcust.sys  <-- PC/TCP stuff
device=c:\qemm\loadhi.sys /r:4 e:\pctcp\ipcust.sys  <-- etc


 A second, more elaborate example, with names easier to type. We start with
file PROTOCOL.INI. Note that semicolons start comment lines.

; This is a sample protocol.ini file listing three Ethernet boards:
;	attcsma.dos is an AT&T StarLAN 10 EN100
;	elnkii.dos  is a 3Com 3C503
;	wd8003.dos  is a Western Digital WD8003E
; Only one board will be selected but the other two are present.

[protocol manager]
    drivername = PROTMAN$

; Packet Driver protocol users tie in here
[pktdrv]
	drivername = pktdrv$
	bindings = attcsma
;	bindings= elnkii
;	bindings = wd8003
	intvec = 0x60
;	chainvec = 0x66		; chaining to another Packet Driver is unused

; AT&T StarGROUP protocol stack ties in here via name ATTISO$
[attiso]
	drivername = ATTISO$
	bindings = attcsma
;	bindings = elnkii
;	bindings = wd8003
	nsess = 5
	ncmds = 14
	use_emm = n

;Western Digital EtherCard PLUS Family Adapter, WD8003E in this case
[wd8003]
	drivername = MACWD$
	irq = 7
	ramaddress = 0xCA00
	iobase = 0x280
	receivebufsize = 1536
;	maxtransmits = 6
;	receivebuffers = 6
;	receivechains = 6

; 3Com Etherlink II, 3C503
[elnkii]
	drivername = ELNKII$
	ioaddress = 0x350
	interrupt = 5
	transceiver = onboard
	maxtransmits = 12
	xmitbufs = 1

; AT&T StarLAN 10 EN100
[attcsma]
	drivername = ATTCSMA$
	board_type = 2
	irq = 2
	ioaddr = 0x360
	daram = 0xD000

; End of file protocol.ini

Fragment of config.sys for the second example. Note three .dos board drivers.

device=c:\system\ramdrive.sys 1024 512 128 /E
device=c:\lanman\protman.sys /i:c:\lanman.dos\drivers\star10en
device=c:\lanman\attcsma.dos
device=c:\lanman\elnkii.sys
device=c:\lanman\macwd.dos
device=c:\lanman\dis_pkt.dos
device=c:\lanman.dos\drivers\attload.dos /Y
device=c:\lanman.dos\drivers\attiso\attiso.dos
device=c:\qemm\loadhi.sys /r:1 e:\pctcp\ifcust.sys
device=c:\qemm\loadhi.sys /r:4 e:\pctcp\ipcust.sys
device=c:\qemm\loadhi.sys /r:4 c:\netdev.sys
shell=c:\command.com  /p /e:800

It seems to be necessary to run NETBIND.EXE to get all this to be active.



Copyright notice and disclaimer from the beginning of the source code
file dis_pkt.asm:

DIS_PKT.ASM - Adapter provides Packet Driver v1.09 interface over NDIS.
Version 1.07  18 May 1991  by Joe R. Doupnik, Utah State Univ.
Copyright (C) 1988 - 1991 FTP Software, Inc.

This unmodified source file and it's executable form may be used and
redistributed freely.  The source may be modified, and the source or
executable versions built from the modified source may be used and
redistributed, provided that this notice and the copyright displayed by
the exectuable remain intact, and provided that the executable displays
an additional message indicating that it has been modified, and by whom.

FTP Software Inc. releases this software "as is", with no express or
implied warranty, including, but not limited to, the implied warranties
of merchantability and fitness for a particular purpose.

USE AT YOUR OWN RISK.

To build, using Microsoft MASM 5.10, LINK 3.64 and EXE2BIN:

masm dis_pkt;
link dis_pkt;
exe2bin dis_pkt.exe dis_pkt.dos
del dis_pkt.exe
del dis_pkt.obj



Here is an excerpt from the formal NDIS v2 specification document by 3Com
and Microsoft concerning what goes into the PROTOCOL.INI file.
 
 PROTOCOL.INI
 The PROTOCOL.INI file stores configuration and binding
 information for all the protocol and MAC modules in the system.
 The file uses the same general format as the LANMAN.INI file.  It
 consists of a series of named sections, where the section name is
 in fact the module name from a module characteristics table.
 Below the bracketed module name is a set of configuration
 settings for the module in name=value format.
 For example:
 
 [MYNetBIOS]
 Drivername = NetBIOS$
 Bindings = ETHERCARD
 MaxNCBs = 16
 MaxSessions = 32
 MaxNames = 16
 
 The rules for PROTOCOL.INI contents are:
 
 o Bracketed module name.  Must be the name of a protocol or MAC
   module, e.g. [MYNetBIOS].  This is the name of the module as
   defined in that module's characteristics table.  The name must
   be 15 characters or less (not counting the brackets).  Mixed
   case may be used but the Protocol Manager will convert it to
   uppercase when it reads the file into memory.
 
 o Drivername = <device driver name>.  This parameter is required
   for all device driver modules.  It defines the name of the OS/2
   or DOS device driver that the module is contained in.  Note
   that a single device driver name may be mentioned by several
   sections of the PROTOCOL.INI file, if the driver contains
   multiple logical modules.  The Drivername parameter is the
   recommended method by which a module searches for its module
   section in the PROTOCOL.INI file to get its configuration
   parameters.  This allows the module to find all relevant module
   sections based on a single name intrinisic to the module
   independent of the particular bracketed module name used in the
   PROTOCOL.INI file.  This keyword is also required for DOS
   dynamic modules like TSRs or transient application modules.
   Although there is no driver name instrinsically assigned to
   such modules it is required that a unique name be assigned to
   this keyword for such modules anyway.  In this way the same
   search mechanism used by device drivers can be used by dynamic
   DOS modules to find their relevant module sections in
   PROTOCOL.INI.
 
 o Bindings = <module name> | <module name>,<module name>, . . .
   This parameter is optional for protocol modules.  It is not
   valid for MAC modules.  If present, it is used by the protocol
   module to determine what MAC modules it will ask to bind to.
   (In other words, changing this parameter in the PROTOCOL.INI
   file can reconfigure a protocol to bind to a different MAC.).
   The Bindings parameter may be omitted if the protocol driver
   software is preconfigured to bind to a particular MAC, or if
   the system will only contain one MAC and one static protocol
   module.  In the latter case (only in static mode), the Protocol
   Manager by default will ask the one static protocol to bind to
   the one MAC.
 
 o Other keywords and parameters.  Any other keyword=value
   statements are module specific.  Keyword names must be 15
   characters or less.  They may be mixed case but are converted
   to uppercase when read by the Protocol Manager.  Note that
   keyword names are unique within the scope of each <module name>
   section and can appear within the section in any order.
 
 o Whitespace around the equals sign is not significant, nor is
   trailing white space on the line.  Except for this leading and
   trailing white space, all other characters of the value string
   are taken verbatim.
 
 o A list of 0 or more parameters can appear to the right of the
   equals sign.  If there are no parameters the equals sign can be
   optionally omitted.  A parameter is terminated by a space, tab,
   comma, or semicolon.  No parameters are interpreted by the
   Protocol Manager.
 
 o A parameter can either be up to a 31-bit signed numeric value
   or a string of any length.
 
 o A numeric parameter can be expressed either in decimal or
   hexadecimal format.  All numeric parameters must start with the
   characters '0' through '9' or by a + or - followed by the '0'
   to'9' character.  A hexadecimal parameter must start with '0x'
   or '0X' and use valid hexadecimal digits.  A non-hexadecimal
   numeric parameter is treated as decimal integer.  A parameter
   not surrounded by quotes and starting with 0 to 9 or + and -
   followed by 0 to 9 will be assumed to be a numeric parameter.
 
 o A string is a parameter which either starts with a non-numeric
   character or is surrounded with quotes ("....").  The string is
   preserved in the memory image as it appears in PROTOCOL.INI.
 
 o A line starting with a semicolon in column 1 is a comment and
   is ignored.  Blank lines are ignored too.
 
 o Lines may be as long as required.  Continuation lines are not
   supported.  Lines end with CR LF.
 
 o Tabs, formfeeds, and spaces are considered to be white space.
 
 The Protocol Manager supports an optional section with optional
 keywords defined below:
 
 [PROTMAN]
 Drivername = PROTMAN$
 Dynamic = YES or NO
 PRIORITY = prot1, prot2, ...
 Bindstatus = YES or NO

  
 The bracketed module name can be any valid name as long as it is
 unique within this PROTOCOL.INI.  Drivername is required and must be
 assigned PROTMAN$, identifying the section as belonging to the
 Protocol Manager.  None of the entries are case-sensitive.
 
 The DYNAMIC keyword is optional.  It defaults to NO if not present.
 If set to NO, the Protocol Manager operates only in the static mode
 and does not support dynamic protocol drivers.  If set to YES, the
 Protocol Manager operates in the dynamic mode and supports both
 static and dynamic binding.
 
 The PRIORITY keyword is optional.  If absent, then the VECTOR uses
 default demultiplexing priority if multiple protocol drivers are
 bound to the same MAC (see Vector Demultiplexing in Chapter 7).  If
 present, the parameters on the right-hand side are presumed to be a
 list of protocol module names, highest priority first.  The VECTOR
 prioritizes protocol drivers for demultiplexing (if necessary)
 according to their order in the list, and packets are offered to the
 first protocol driver listed first.  Protocol drivers not listed are
 assigned default priority AFTER those listed.  It is not necessary
 that a protocol driver ever bind for it to be listed here.
 
 The BINDSTATUS keyword is optional.  If absent, then the BindStatus
 command is not supported by the Protocol Manager.  If set to YES,
 then BindStatus is supported by the Protocol Manager.  The default
 disable condition is a memory optimization feature primarily for DOS
 environments.
 
;;;;;;;;;;; End of file DIS_PKT.DOC